| Construction Detail | Product Illustration |
| --- | --- |
| Physical Construction | Description |
| Component 1: 16 AWG 65/34 bare copper conductor SR-PVC Insulation: .016-inch nominal thickness | Communications rated multi-conductor wire for control, instrumentation and distributed audio applications in accordance with NEC article 800. |
|  | Color Code |
|  | Black, Red, White, Green |
|  | Electrical Specifications |
|  | 16 AWG: DCR: 4.878 ( per 1000 feet Voltage: 300 Volts RMS Temperature: -20(C to 75(C |
| Final assembly: 4 of component 1 twisted in a 4-inch lay Nylon ripcord under the jacket. PVC jacket: .025-inch nominal thickness Final construction: .280-inch nominal OD Product Print Legend: KO PLUS™ BY LIBERTY 16-4C-KO+ E190606-J (UL) 16 AWG TYPE CM 75(C --- C(UL) TYPE CMG 60(C Sequential footmarks are applied in conjunction with the print legend. | Regulatory Specifications |
|  | (UL) rated CM C(UL) rated CMG EU RoHS 2002/95/EC Compliant since 08/26/2003 |
| Specification Control | Product Information |
| Revision Date: 08/26/2003 Liberty Wire & Cable specifications are subject to change without notice. Contact an account representative for current product specifications. Liberty Wire & Cable continuously strives to ensure product specifications are accurate and complete. All physical specifications are nominal. | Jacket Colors: Light Green, White, Hot Pink, Gray Packaging: 1000 foot reels, 500 foot reels, 500 ft pull box |